## Slide 1: Coshh awareness

## Slide 2
Classified
    Irritant, harmful, corrosive, toxic, carcinogenic
Wel
    Workplace exposure limit (8 hours, 15mins)
Biological agents
    Fungi, moulds, bacteria, viruses
Substantial dust
    Fine = more risk, respirable dust, concrete

## Slide 3
COSHH requirements do not apply to;
  Asbestos
  Lead
  Radiation
  Explosives
  Medication
Not because they are safe, but because they have their own regulations.

## Slide 4
Employer requirements under the COSHH regulations.
The eight steps
  Assess risks
  Decide on precautions
  Prevent or control exposure
  Ensure control measures used & maintained
  Monitor exposure
  Carry out health surveillance
  Prepare for accidents and emergencies
  Ensure employees are informed, trained and supervised.

## Slide 5
Before we can do this, we must appreciate how various substances affect those at work
    Ways the substances can enter our systems
    How our bodies protect us
    What the potential effects are
    What the different classifications mean
    How each different classified substance causes harm
    Safe practice upon exposure

## Slide 6
Routes of Entry to the body?
  Inhalation
  Absorption
  Injection / Puncture Wounds
  Ingestion

## Slide 7
Inhalation;
  Breathing in with normal air intake
  Main route of entry
  Chemical (solvents, welding fumes) or biological (bacteria or fungi)
  Sweeping, spraying
  Enter lungs, pass to bloodstream – access all areas!

## Slide 8
Absorption;
  Contact with skin
  Enters through pores or a wound
  Tetanus, (rusty nails) benzene (petroleum)
  Direct access to bloodstream

## Slide 9
Ingestion;
  Through the mouth
  Through to digestive system
  Airborne dust
  Poor hygiene!

## Slide 10
Injection;
  Air bubbles
  Syringes – abused
  HIV, hepatitis

## Slide 11
Needle stick injuries;
  Don’t put your hands anywhere you can’t see
  If you come across needles report to your supervisor
  Do not handle the needle unless you are appropriately trained

## Slide 12
Needle stick injuries;
  Wash well under cold running water without soap and cover with a dry dressing
  Do not suck the wound
  ‘Bleed’ the wound if able
  Accompany to nearest A & E, taking needle in puncture proof container if possible.

## Slide 13
Natural defences
  Skin
  Vomit
  Stomach acid
  Liver / kidneys
  Sneeze / cough
  Cillary hairs

## Slide 14
Potential health risks
  Diseases of the skin
  Diseases of the respiratory system
  Cancer and birth defects
  Asphyxiation
  Central nervous system disorders
  Specific organ damage

## Slide 15
Effects on health may be either acute or chronic
  Acute;
    Short duration, appear rapidly
    After short term exposure
    Nausea, fainting, asthma attacks
  Chronic;
    Develop over a log period of time (no symptoms?)
    Prolonged or repeated exposures
    Cancers, mental illness

## Slide 16
Irritant;
  Can cause dermatotic or bronchial inflammation
  After repeated contact
  Concentration more likely damage than exposure time
  Bleaches, glues, solvents

## Slide 17
Harmful;
  Most common
  May pose risk if swallowed, inhaled or penetrates the skin
  Bitumen-based paints, trichloroethylene & other chemical cleansers

## Slide 18
Toxic or very toxic;
  Impede function of organs (kidneys, liver, heart etc)
  Poisonous
  Mercury, pesticides

## Slide 19
Corrosive;
  Attacks living tissue
  Normally by burning
  Usually strong acid or alkali
  Oven cleaners, dishwasher crystals

## Slide 20
Carcinogenic;
  Promote cancers
  Abnormal development of body cells
  Asbestos, creosote

## Slide 21
Safe practice – harmful substance
  Contact with eyes?
    Rinse immediately with plenty of water, seek medical advice
  Wash thoroughly before eating, drinking or smoking
  Do not breath vapour / spray / dust
  Avoid all contact

## Slide 22
Safe practice – corrosive substance
    Wear suitable gloves and eye / face protection
    Immediately remove contaminated clothing
  Contact with eyes?
      Rinse immediately (for 15 minutes) with plenty of water, seek medical adviceContact with skin?
      Wash immediately with plenty of water
      Avoid all contact

## Slide 23
Safe practice – toxic / very toxic substance
    Wear suitable PPE (clothing, gloves, eye / face protection)
  Contact with eyes?
      Rinse immediately with plenty of water, seek medical advice
  Contact with skin?
      Wash immediately with plenty of water
  In case of accident, or if you feel unwell, seek medical advice immediately
  Avoid all contact

## Slide 24
Storage
  Some materials must not be stored together.
    The safety data sheet will list materials which have to be segregated.
    HSE’s “storing packaged dangerous substances: segregation table” gives further guidance

## Slide 25
Conclusion
    Ensure you are happy with all of the information related to a substance
    Ensure you are happy that the ‘8 steps’ have been followed
      And controls are in place!
      And controls are relevant!
    Do not assume a substance is safe
    Ensure you know where to access the relevant information.