## Slide 1: FIRE SAFETY AT WORK

## Slide 2: Death and Destruction
What is it that kills people in the event of a fire?
SMOKE kills
Burns
Heat

## Slide 3: Death and Destruction
In the UK 2019 / 20;
153,957 fires attended by Fire Service. (36% less than 10 years ago)
243 fire-related deaths
68,677 primary fires (14,308 in non domestic properties

## Slide 4
The rapid oxidation of fuel evolving heat, particles, gases and non-ionising radiation
A self sustaining chemical reaction involving the bonding of oxygen with carbon and other fuels
Q. What is fire?

## Slide 5
Red Flame
Between 5250 C < 10000 C
Orange Flame
11000 C < 12000 C
White Flame
15000 C
Fire Facts

## Slide 6
Nature of Fire
Three Basic Ingredients Necessary For Fire:
Oxygen
Heat
Fuel

## Slide 7
Heat
Created by a source of ignition
Naked Flames
External Sparks – Welding etc
Internal Sparks – Lighting etc

## Slide 8
Heat
A critical temperature must be reached for ignition to take place.
Once a fire has started, it will generally maintain its own heat supply.
Flash Point
Lowest temperature at which vapour is released in sufficient quantity for combustion, if ignited.
Auto ignition
Temperature at which it will catch fire without ignition

## Slide 9
Fuel
Any combustible substance, whether solid, liquid or gas.

## Slide 10
Oxygen
Oxygen is present in the air, approximately 21% at sea level
A level of only 16% is needed to support a fire

## Slide 11
Fire Spread
Conduction
Convection
Radiation

## Slide 12
Heat is transferred through solid material such as a metal beam
Conduction

## Slide 13
Convection
Hot air and smoke rises upwards into the atmosphere. Why?
Hot air less dense, drawing in cold air and oxygen
e.g. bonfire or convector heater

## Slide 14
Radiation
Direct heat travels through emission of heat waves from a source such as the sun or the bars of an electrical fire

## Slide 15
Three States of Matter
Solid Liquid Gaseous

## Slide 16
D
Solid Materials: Water, Foam, Powder Wood, paper, textiles, fabric
Liquid/liquifiable solids: Foam, Powder, CO2 Petrol, Diesel Oils
Fires involving Gases: Powder Butane, Methane, Propane
Fires involving Metals: Pyromet Powder Lithium, magnesium, sodium or aluminium
Electrical Risk CO2 Computers, Switchgear, Fax
Cooking Oil (3+litres) Wet Chemical
Classification of Fires

## Slide 17
Starvation
Oxygen
Heat
Fuel
Smothering
Cooling
Three Methods of Extinction

## Slide 18
Smothering
Removal or limitation of oxygen
  Snuffing out a candle, covering a chip pan fire
  Liquid fires will extinguish if oxygen level is reduced below 16%
  Solid materials may continue to burn until a drop to 6%.
  Some substances carry enough oxygen to maintain combustion

## Slide 19
Cooling
Removal of heat
  Water is most commonly used, as it has great heat absorbing properties.
  If rate of heat lower than rate of heat absorbed, the fire will go out.

## Slide 20
Starving
Removing a fire’s fuel supply will extinguish a fire
  Turning off gas supplies
  Removal of Fuel

## Slide 21: Portable Fire Extinguishers
WARNING: Do not use on Electrical Hazards!
WARNING: Do not use on ‘Class B’ Flammable Liquid fires
Water

## Slide 22: Portable Fire Extinguishers
FOAM
2, 6 and 9 litre
Stored Pressure & Cartridge Operated
Some have added Operator Safety of 35kv test

## Slide 23: Portable Fire Extinguishers
CO2
2 and 5kg
Clean medium
WARNING: Nozzle gets very cold during use!
Thickened horn can be fitted to protect against frost burns

## Slide 24: Portable Fire Extinguishers
1, 2, 3, 6 and 9kg
All round safety
Dry Powder

## Slide 25: Portable Fire Extinguishers
Water with Additive
6 and 3 litre
Stored Pressure
User-friendly
Often same fire fighting capacity as 9 litre water

## Slide 26: Portable Fire Extinguishers
Wet Chemical

## Slide 27: Fighting a Fire
Do not fight the fire if:-
  It is bigger than a waste paper bin
  One extinguisher is not enough
  Smoke is affecting your breathing
  You cannot see the way out
  Gas cylinders or chemicals are involved
  Your efforts are not reducing the size of the fire
  Always keep an exit available when tackling a fire
  Generally, fight the fire to ensure successful evacuation

## Slide 28: Remember - If tackling a fire!
IRE BRIGADE?
S IT SAFE TO TACKLE THE FIRE?
IGHT TYPE OF FIRE EXTINGUISHER?
XIT ROUTE CLEAR